### Eco Driving Course, City Way School of Motoring

### What will I Learn On The Course?

On the course your instructor will help you to drive in a smoother more planned way, not only helping to reduce your motoring costs but also making your journeys safer. Some examples of the many techniques taught are below:

### Revs and Gears

All engines are at their most fuel efficient at lower revs; to keep your engine revs low you will be encouraged to change up the gears earlier and also avoid unnecessary gear changes.

### Planning Your Braking

Fuel savings can also be made by braking gently and spreading your braking evenly; to avoid heavy or unnecessary braking your instructor will give you tips on how to look ahead more and plan your speed adjustments.

### Anticipate

You will learn how to anticipate road conditions and drive smoothly, avoiding sharp acceleration and looking well ahead by forward planning.

### Some Fuel saving Tips:

- Maintain a constant speed if the traffic and road conditions allow. The most fuel efficient speed for most cars is around 45 - 55mph.

- When stuck in a traffic queue for more than a minute switching off the engine will save fuel and reduce emissions

- Avoid using your cars air conditioning system unnecessarily; using air conditioning for long periods significantly increases fuel consumption

- Plan your journeys to avoid busy times, road works and getting lost!

- Avoid short journeys your car is least efficient when it's cold, it can take up to 7 miles for a vehicle to reach its optimum temperature

- Keep a regular check on your tyre pressures, this is very important for driving safety and can also save you around 3% on your fuel costs – also consider Low rolling resistance tyres, the next time you change your tyres.

- Keeping your windows and sunroof closed will make your car more aerodynamic; also remove roof racks and bike carriers when they are not being used

- Modern engines don't need to be warmed up before you set off - just start up and go, but only start your vehicle when your ready to go.

- Avoid driving with unnecessary weight in your car as this will make your engine work harder and use more fuel